## Slide 1: Planning in Continuous Spaces: Motion Planning
Tom Silver
Robot Planning Meets Machine Learning
Princeton University
Fall 2025

## Slide 2: Recap and Preview
Earlier:
Planning in finite “tabular” state and action spaces
Careful treatment of uncertainty in transitions and observations
Offline planning and online planning
Last Time:
Planning in finite “factored” state and action spaces
No more uncertainty
Online planning only
This Time:
Planning in continuous spaces
But with a very specific structure

## Slide 3: Motion Planning
Skydio (2019)
Kuffner (2002)
Realtime Robotics (2023)

## Slide 4: Motion Planning Problem Setting
A motion planning problem includes:
A configuration space
An initial configuration
A goal configuration
A feasibility check
Must be bounded & have distance metric & have other nice properties…
Alternative definition: set of configurations
Usually: feasible (T) if robot not in collision

## Slide 5: Motion Planning Solution
A solution to a motion planning problem is a trajectory
where
The robot can follow the trajectory
Many different ways to specify this
Continuous states and continuous time!
Actions are now implicit

## Slide 6: Example: Motion Planning with 2D Shapes
Configuration space:
  (x position, y position, rotation)
  x and y position are bounded
  Subset of SE(2)
Initial configuration: see image
Goal configuration: see image
Feasibility check:
  Configuration is feasible if robot is not in collision with obstacles

## Slide 7: A Stupidest Possible Algorithm
Discretize the configuration space
Run path planning (e.g., A* with distance-to-goal heuristic)
When will this go badly?
Is this sound, complete, optimal?

## Slide 8: A “Bug Algorithm”
At each time step:
If can move directly towards goal, do so
Otherwise, move ccw around obstacle

## Slide 9: A “Bug Algorithm”
At each time step:
If can move directly towards goal, do so
Otherwise, move ccw around obstacle

## Slide 10: A “Bug Algorithm”
At each time step:
If can move directly towards goal, do so
Otherwise, move ccw around obstacle

## Slide 11: A “Bug Algorithm”
At each time step:
If can move directly towards goal, do so
Otherwise, move ccw around obstacle

## Slide 12: A “Bug Algorithm”
At each time step:
If can move directly towards goal, do so
Otherwise, move ccw around obstacle

## Slide 13: A “Bug Algorithm”
At each time step:
If can move directly towards goal, do so
Otherwise, move ccw around obstacle

## Slide 14: A “Bug Algorithm”
At each time step:
If can move directly towards goal, do so
Otherwise, move ccw around obstacle

## Slide 15: A “Bug Algorithm”
At each time step:
If can move directly towards goal, do so
Otherwise, move ccw around obstacle

## Slide 16: A “Bug Algorithm”
At each time step:
If can move directly towards goal, do so
Otherwise, move ccw around obstacle

## Slide 17: A “Bug Algorithm”
At each time step:
If can move directly towards goal, do so
Otherwise, move ccw around obstacle

## Slide 18: A “Bug Algorithm”
At each time step:
If can move directly towards goal, do so
Otherwise, move ccw around obstacle

## Slide 19: A “Bug Algorithm”
At each time step:
If can move directly towards goal, do so
Otherwise, move ccw around obstacle

## Slide 20: A “Bug Algorithm”
At each time step:
If can move directly towards goal, do so
Otherwise, move ccw around obstacle

## Slide 21: A “Bug Algorithm”
At each time step:
If can move directly towards goal, do so
Otherwise, move ccw around obstacle

## Slide 22: A “Bug Algorithm”
At each time step:
If can move directly towards goal, do so
Otherwise, move ccw around obstacle

## Slide 23: A “Bug Algorithm”
At each time step:
If can move directly towards goal, do so
Otherwise, move ccw around obstacle

## Slide 24: A “Bug Algorithm”
At each time step:
If can move directly towards goal, do so
Otherwise, move ccw around obstacle
Show that this algorithm is not complete
There are complete bug algorithms

## Slide 25: Sampling-Based Motion Planning
Let’s assume we can sample from the configuration space

## Slide 26: Rapidly Exploring Random Trees (RRT)

## Slide 46
Many interpolation strategies are possible

## Slide 47: Important Hyperparameter: Feasibility Check Distance
Check Distance = 5.0
Check Distance = 1.0
Check Distance = 0.2

## Slide 48: Properties of RRT
Probabilistically complete
Not optimal
Single query
Works with underactuated systems
Works for kinodynamic problems
Has Voronoi bias
The probability of expanding a tree node is proportional to the size of its Voronoi region
https://en.wikipedia.org/wiki/Voronoi_diagram

## Slide 49: Post-Processing with Shortcuts
Repeatedly sample two points on the trajectory and check if a direct line between them is feasible (rewire if so)
Attempts = 0

## Slide 50: Post-Processing with Shortcuts
Repeatedly sample two points on the trajectory and check if a direct line between them is feasible (rewire if so)
Attempts = 0
Attempts = 100

## Slide 51: Post-Processing with Shortcuts
Repeatedly sample two points on the trajectory and check if a direct line between them is feasible (rewire if so)
Attempts = 0
Attempts = 100
Attempts = 10000

## Slide 52: Bidirectional RRT
Grow two trees: one from start, the other from goal
Does not work for underactuated systems

## Slide 53: Demo with 7DOF Robot Arm
https://github.com/rpmml/rpmml-code/blob/mp-pybullet-example/scripts/motion_planning_robot_example.py

## Slide 54: Multi-Query Motion Planning
RRT grows tree once, from initial to goal
After the robot moves, need to start from scratch
Can we build a representation once, up front, instead?
Need a graph instead of a tree

## Slide 55: Probabilistic Roadmaps (PRMs)

## Slide 72
1.25
1.05
1.25
0.65
0.95
1.25
1.05
0.80
1.15
1.00
0.95
0.45
0.55
0.65
1.05
1.05

## Slide 73
1.25
1.05
1.25
0.65
0.95
1.25
1.05
0.80
1.15
1.00
0.95
0.45
0.55
0.65
1.05
1.05

## Slide 74
1.25
1.05
1.25
0.65
0.95
1.25
1.05
0.80
1.15
1.00
0.95
0.45
0.55
0.65
1.05
1.05

## Slide 75
1.25
1.05
1.25
0.65
0.95
1.25
1.05
0.80
1.15
1.00
0.95
0.45
0.55
0.65
1.05
1.05
1.00
0.70
Reuse graph for new query

## Slide 76
1.25
1.05
1.25
0.65
0.95
1.25
1.05
0.80
1.15
1.00
0.95
0.45
0.55
0.65
1.05
1.05
1.00
0.70
Reuse graph for new query

## Slide 77: When and Why Does Sampling-Based Motion Planning Work?
Works well when every configuration “sees” a significant fraction of feasible space
Prototypical bad situation: narrow passages
If interested: there are formal guarantees in terms of -goodness and -lookout

## Slide 78: Implementation Considerations
Example: Sampling uniformly on a sphere requires some thought
Sampling
Need to be careful depending on configuration space
https://extremelearning.com.au/how-to-generate-uniformly-random-points-on-n-spheres-and-n-balls/

## Slide 79: Implementation Considerations
Sampling
Distance metrics
Need to be careful when angles are involved
Example: Weighted distance function in SE(2)

## Slide 80: Implementation Considerations
Sampling
Distance metrics
Nearest neighbors
Can often do better than naïve quadratic algorithm
Example: KD trees (for Euclidean configuration spaces)

## Slide 81: Implementation Considerations
Sampling
Distance metrics
Nearest neighbors
Collision checking
Usually the speed bottleneck. Use existing optimized libraries!

## Slide 82: Implementation Considerations
Sampling
Distance metrics
Nearest neighbors
Collision checking
Interpolation
Linear, polynomial, trapezoidal…